## Slide 1
Background Information
Many vendors already ship items with EPC tags. These UPCs conform to the GS1 standards for UPC creation and assign a Global Trade Item Number (GTIN), therefore, Target’s systems must be able to read these and map the encoded numbers back to an internal Target Corporation Item Number (TCIN) and to possibly many Department Class Item numbers (DPCI). When a serial number is added to a GTIN to uniquely identify the item, it is known as a Serialized GTIN or SGTIN. The GTIN includes:
  Company Prefix: a variable 6 to 12 digit company prefix of the assigning company
  Item Reference: a 7 to 1 digit Item reference and indicator
  Check Digit: 1 digit for barcode check digit (this need not be encoded in EPC tags)
These can be encoded in a 14 digit GS1 barcode. Any 12 digit GTIN used in the US and Canada can be converted to a 14 digit GTIN by prefixing it with two zeros. The first zero is an indicator digit meaning an individual item for retail sale, and the second is the country/region code for the US and Canada. If an item is only meant for sale in this region, these digits can be omitted and the GTIN 12 used.
Vendor Generated UPC Examples:
Vendor Generated EPC Schema
Vendor geneated UPCs for source tagged product will follow the GS1 SGTIN format
http://www.gs1.org/sites/default/files/docs/epc/TDS_1_9_Standard.pdf
6.3.1. Serialized Global Trade Item Number (SGTIN): Page 26
Vendor Generated UPC Encoding Examples:
Note: see http://www.kentraub.net/tools/tagxlate/EPCEncoderDecoder.html for a good tool to validate encodings (use GTIN14 with filter value of 1 – POS Item).
RFID Start-Up Guide
Vendor Generated UPC in SGTIN EPC Schema
(Source Tagging)
URI | GTIN 12 | GTIN 14
urn:epc:id:sgtin:0038000.035621.12345 | 038000356216 | 00038000356216
urn:epc:id:sgtin:0030878.099916.67890 | 030878999168 | 00030878999168
urn:epc:id:sgtin:0085387.030438.12345 | 085387304385 | 00085387304385
Barcode | Company Prefix | ObjectClass (No Check Digit) | Serial Number | SGTIN Hex
00038000356216 | 0038000 | 035621 | 12345 | 30340251C022C94000003039
030878999168 | 0030878 | 099916 | 67890 | 303401E27861930000010932
085387304385 | 0085387 | 030438 | 12345 | 303405362C1DB98000003039

## Slide 2
Background Information
Many of Target’s vendors generate a 49 UPC. Since this is not a globally unique GTIN, an alternate encoding can be used for this 12 digit barcode:
  Positions 1 and 2: 49
  Positions 3-11: Target’s internal financial/merchandising categorization and identification number (DPCI). DPCI is
    3 digit Department
    2 digit Class
    4 digit Item Number
  Position 12: system calculated Check Digit
Target Generated 49 UPC Examples:
Target Generated 49 EPC Schema
Target’s 49 UPC source tagged product will follow a variation of the GS1 GID format
http://www.gs1.org/sites/default/files/docs/epc/TDS_1_9_Standard.pdf
6.3.11. General Identifier (GID): Page 31
Target will follow this construct:
  ManagerNumber: 49 + 3 digit Department + 2 digit Class (always starts with ‘49’)
  ObjectClass: 4 digit Item Number + Check Digit (add leading 0’s till 5 digits)
  SerialNumber: 11 digit, serialized unique ID (add leading 0’s till 11 digits, max 68719476735)
Target uniquely assigns the leading 2 digits of the Serial # to each tag supplier (‘Commissioning Authority”). Please consult a Target representative for your Commissioning Authority ID. Decode the serial number first and reference slide 4 if it begins with 01, 03 or 04.
Target Generated 49 UPC Encoding Examples:
Important note: Using the 49 code and department class for the manager number, not a GS1 assigned Company Prefix, means this is not guaranteed to be globally unique.
RFID Start-Up Guide
Target Generated 49 UPC in GID EPC Schema
(Source Tagging)
Preferred
URI | DPCI | Barcode
urn:epc:id:gid:4928300.16670.5000000001 | 283-00-1667 | 492830016670
urn:epc:id:gid:4902908.8545.5000000002 | 029-08-0854 | 490290808545
urn:epc:id:gid:4902907.15317.5000000003 | 029-07-1531 | 490290715317
Barcode | Manager Number | ObjectClass (w/Check Digit) | Serial Number | GID Hex (drop leading zeros before encoding)
492830016670 | 4928300 | 16670 | 05000000001 | 3504B332C00411E12A05F201
490290808545 | 4902908 | 08545 | 05000000002 | 3504ACFFC00216112A05F202
490290715317 | 4902907 | 15317 | 05000000003 | 3504ACFFB003BD512A05F203

## Slide 3
Background Information
Some vendors ship items with EPC tags that encode our target 49 barcodes with the GS1 standard SGTIN format. These SGTINs are not global GTINs, but it is acceptable GS1 practice to use barcodes that begin with 49 for internal use. These SGTINs can be unpacked to get the associated DPCI:
  Positions 1 and 2: 49
  Positions 3-11: Target’s internal financial/merchandising categorization and identification number (DPCI). DPCI is
    3 digit Department
    2 digit Class
    4 digit Item Number
  Position 12: system calculated Check Digit
These can be encoded in a 14 digit GS1 barcode. Any 12 digit GTIN used in the US and Canada can be converted to a 14 digit GTIN by prefixing it with two zeros. The first zero is an indicator digit meaning an individual item for retail sale, and the second is the country/region code for the US and Canada. If an item is only meant for sale in this region, these digits can be omitted and the GTIN 12 used.
Target Generated 49 UPC Examples:
Target Generated 49 EPC Schema (Alternate – NOT preferred)
Target’s 49 UPC source tagged product may also follow the GS1 SGTIN format
http://www.gs1.org/sites/default/files/docs/epc/TDS_1_9_Standard.pdf
6.3.1. Serialized Global Trade Item Number (SGTIN): Page 26
Target Generated 49 UPC Encoding Examples (Alternate):
Note: see http://www.kentraub.net/tools/tagxlate/EPCEncoderDecoder.html for a good tool to validate encodings (use GTIN14 with filter value of 1 – POS Item).
RFID Start-Up Guide
Target Generated 49 UPC in SGTIN EPC Schema
(Source Tagging)
Deprecated – Do NOT USE Going Forward
URI | GTIN 12 | GTIN 14
urn:epc:id:sgtin:0498000.035621.12345 | 498000356216 | 00498000356216
urn:epc:id:sgtin:0490878.099916.67890 | 490878999168 | 00490878999168
urn:epc:id:sgtin:0495387.030438.12345 | 495387304385 | 00495387304385
Barcode | Company Prefix | ObjectClass (No Check Digit) | Serial Number | SGTIN Hex
00498000356216 | 0498000 | 035621 | 12345 | 30341E6540037A8000003039
490878999168 | 0490878 | 099916 | 67890 | 30341DF5F861930000010932
495387304385 | 0495387 | 030438 | 12345 | 30341E3C6C1DB98000003039

## Slide 4
Background Information
If a tag is lost (either for returned product, or missing from a sales floor item), the Store team will provision a replacement tag. For vendor generated UPCs, we won’t be able to assure a unique serial number to create a new SGTIN. As we are the provisioning authority for our 49 UPCs, we can provision a replacement tag that will be unique. Both vendor generated UPC and Target generated 49 UPC replacement tags will be based on the original UPC code to be replaced:
  UPC: 12 digit barcode (for Target generated UPCs, this starts with 49)
  GTIN: 00 + barcode
Examples (original, not replacement):
In Store Retagging in GID EPC Schema
In store replacement tags for both vendor generated UPCs and and Target generated 49 UPCs will follow a variation of the GS1 GID format
http://www.gs1.org/sites/default/files/docs/epc/TDS_1_9_Standard.pdf
6.3.11. General Identifier (GID): Page 31
Target will follow this construct:
  ManagerNumber: Digits 1 through 8 of UPC (add leading 0’s till 8 digits)
  ObjectClass: Digits 9 through 14 of UPC (add leading 0’s till 6 digits, includes check digit)
  SerialNumber: 11 digit, serialized unique ID (add leading 0’s till 11 digits, max 68719476735)
Target uses one of the reserved Commissioning Authority numbers (first two digits of serial number) for these tags: 01, 03 or 04. Decode the serial number first and reference slide 2 if it DOESN’T begin with 01, 03 or 04.
Encoded Replacement Tag Examples:
Important note: Using the shifted UPC (GTIN) for the manager number, not a GS1 assigned Company Prefix, means this is not guaranteed to be globally unique.
RFID Start-Up Guide
In Store Retagging in GID EPC Schema
(Retagging)
Target Internal Use Only
URI | UPC/GID
urn:epc:id:sgtin:0038000.035621.12345 | 00038000356216
urn:epc:id:sgtin:0030878.099916.67890 | 00030878999168
urn:epc:id:gid:4928300.16670.1000000001 | 00492830016670
Barcode | Manager Number | ObjectClass (w/Check Digit) | Serial Number | GID Hex (drop leading zeros before encoding)
00038000356216 | 00038000 | 356216 | 04000000001 | 350009470056F780EE6B2801
030878999168 | 00030878 | 999168 | 04000000002 | 35000789E0F3F000EE6B2802
492830016670 | 00492830 | 016670 | 04000000003 | 35007851E00411E0EE6B2803

## Slide 5
Background Information
As Target continues to refactor our internal systems to enable an omnichannel supply chain, we will begin to leverage the Target Corporation Item Number (TCIN). This is a random 10 digit number assigned by our new Product Information Management system (PIM) and is currently used by our online properties. The TCIN identifies an item at a more granular level than the DPCI, and allows for correct identification of the exact product that the guest desires (e.g. Batman vs. Superman costume, which may be the same DPCI).
As this is a random 10 digit number, there is no logic built into the TCIN, and the number itself cannot identify the item without referring to the product catalog. The TCIN is not represented in barcode format.
Example TCINs:
Target Common Item Number EPC Schema
Target will use the modified GS1 Global Individual Asset Identifier GIAI format for TCINs
http://www.gs1.org/sites/default/files/docs/epc/TDS_1_9_Standard.pdf
6.3.5. Global Individual Asset Identifier (GIAI): Page 28
Target will follow this construct:
  ManagerNumber: 10 digit TCIN (add leading 0’s till 10 digits)
  SerialNumber: 15 digit, serialized unique ID (add leading 0’s till 15 digits)
Target will have the leading 2 digits of the Serial # be unique to each tag supplier (‘Commissioning Authority”). Please consult a Target representative for your Commissioning Authority ID. Per GS1 standards, the Serial number must start with a non zero digit, so pad with leading zeroes AFTER decoding.
Target Examples:
Important note: Using the TCIN for the manager number, not a GS1 assigned Company Prefix, means this is not guaranteed to be globally unique.
RFID Start-Up Guide
Target Common Item Number EPC Schema
URI | Description | TCIN
urn:epc:id:giai:0013951442.10000000000001 | Waterpik DSL-653 | 13951442
urn:epc:id:giai:0014448.79610000000000002 | Oster DuraCeremanic Waffle Iron | 14448796
urn:epc:id:giai:0016399080.10000000000003 | GoPro Hero4 Silver Edition | 16399080
TCIN | Manager Number | Serial Number | GID Hex (drop leading zeros of SN before encoding)
13951442 | 0013951442 | 010000000000001 | 340800D4E1D209184E72A001
14448796 | 0014448796 | 010000000000002 | 341400E1C11AD4DF8A91A002
16399080 | 0016399080 | 010000000000003 | 340800FA3AE809184E72A003

## Slide 6
RFID Start-Up Guide
Commissioning Authority IDs
ID | Authority | Encode/Decode | Notes
00 | Reserved TGT Internal | Slide 2 | No Use Yet
01 | Reserved TGT Internal | Slide 4 | Retagging - No Use Yet
02 | Checkpoint | Slide 2 | Source/Supply Chain/In Store Tagging
03 | Reserved TGT Internal | Slide 4 | Retagging - No Use Yet
04 | Reserved TGT Internal | Slide 4 | Retagging - No Use Yet
05 | Avery Dennison | Slide 2 | Source Tagging
06 | SML | Slide 2 | Source Tagging
07 | SML | Slide 2 | Source Tagging
08 | Checkpoint | Slide 2 | Source Tagging - No Use Yet
09 | [Open] |  | 
10 | Reserved TGT Internal | Slide 5 | TCIN + Serial Number
11 | Reserved TGT Internal | Slide 5 | TCIN + Serial Number
12 | Reserved TGT Internal | Slide 5 | TCIN + Serial Number
13 | Reserved TGT Internal | Slide 5 | TCIN + Serial Number
14 | Ceva | Slide 2 | Source Tagging
… | [Open] |  | 
67 | [Open] |  | This is the maximum available
NOTE: None of the reserved retagging IDs on Slide 4 are currently used (01, 03, 04).
NOTE: Max ID is 67, as serial numbers beginning with 68 for GID encodings can only go up to 68719476735 due to limitations in the number of bits in the binary encoding.